＋Performance

| Model | P4305 | P4603 |
| --- | --- | --- |
| Channel | Single Channel Output |
| Total Output Power | 150W | 180W |
| Channel Output | 0 - 30V / 0 - 5A × 1-CH | 0 - 60V / 0 - 3A × 1-CH |
| Display | 3.7 inch color LCD display |
| Dimension | 117mm(L) × 194mm（H）× 295mm（D） |
| Weight | Approx. 5.6 kg | Approx. 5.8 kg |
| Interface | RS232 |

The instrument must be operated continuously for more than 30 minutes at the specified temperature to ensure the following parameters.

| Model | P4305 | P4603 |
| --- | --- | --- |
| Rated Output（0℃-40℃） | Voltage | 0 - 30V | 0 - 60V |
|  | Current | 5A | 3A |
| Load Regulation | Voltage | ≤0.01%+3mV |
|  | Current | ≤0.01% + 3mA |
| Power Regulation | Voltage | ≤0.01% + 3mV |
|  | Current | ≤0.01% + 3mA |
| Setting Resolution | Voltage | 1mV |
|  | Current | 1mA |
| Readback Resolution | Voltage | 1mV |
|  | Current | 1mA |
| Setpoint accuracy （within 12 month） （25℃±5℃） | Voltage | ≤0.03% + 10mV |
|  | Current | ≤0.1% + 5mA |
| Readback Resolution （25℃±5℃） | Voltage | ≤0.03% + 10mV |
|  | Current | ≤0.1% + 5mA |
| Ripple/Noise （20Hz-20MHz） | Voltage（Vp-p） | ≤4mVp-p |
|  | Voltage（rms） | ≤1mVrms |
|  | Current（rms） | ≤4mArms |
| Output temperature coefficient （0℃-40℃） | Voltage | ≤0.03% + 10mV |
|  | Current | ≤0.1% + 5mA |
| Readback temperature coefficient | Voltage | ≤0.03% + 10mV |
|  | Current | ≤0.1% + 5mA |
| Response Time | 100 μs |
| Storage | 5 group data |
| Working Temperature | 0-40℃ |

The above parameters are subject to change without further notice, please refer to the website update.

＋Application

Military R&D  Quality Inspection  Circuit Functional Testing  Automotive Circuit Testing  Education and Technical Training

Electronic component testing and aging experiment  Monitoring battery charging curve

＋Main Accessories The picture is for reference only, please refer to the actual product

Power Cord           User Manual         Fuse        Test Leads (optional)   RS232 TO USB Module ( optional )

# Text boxes

P4000 Series Single Channel Linear DC Power Supply

+ Small body for easy carry

+ 180W maximum output power

+ High resolution： 1mV / 1mA

+ Low ripple/noise

+ Over voltage/over current protection

+ Multi-directional cooling system with smart fan

+ 3.7 inch TFT LCD display

+ Support RS232 digital communication

+ Support SCPI and Labview